## Slide 1
ANDROID
Sensing the User's World
Every 5 seconds, the phone samples nearly everything it knows about itself.
Motion
Accelerometer, gyroscope,
rotation, magnetometer
Environment
Barometer, light,
proximity, humidity
Location
GPS: position, speed,
altitude, bearing
Device State
Battery, screen, DND,
Bluetooth, WiFi
Activity
Inferred: walking, running,
in vehicle, still

## Slide 2
ANDROID
From Sensors to a Live Feed
1
Collect
Sample every 5 seconds
2
Snapshot
Build a JSON payload
3
Serve
HTTP server on-device
4
Fetch
Teammates pull it in
$ curl http://<phone-ip>:8080/context Runs as a background service — persistent notification, survives closing the app.

## Slide 3
ARDUINO
The Physical Sensor Board
An Arduino UNO Q: one board, two processors, wired to real sensors.
MCU · STM32
Runs the sketch — reads sensors in real time.
MPU · Linux
Runs Python — App Lab orchestrates both sides.
Bridge
(RPC)
Sensors on board (I2C / Qwiic)
Modulino Thermo
Temperature, °C
Modulino Distance
Time-of-flight distance, mm

## Slide 4
ARDUINO
Sketch → RPC → HTTP Feed
Read
Sketch reads Modulino sensors
Expose
Bridge.provide() shares them
Poll
Python calls Bridge.call()
Serve
JSON on port 9000
$ curl http://<uno-q-ip>:9000/data { "temperature": 27.8, "distance": 36, "timestamp": "2026-08-06 14:32:07" }

## Slide 5
LLM
A Local AI Interprets the Readings
Raw sensor + phone JSON goes in; a short, plain-language summary comes out.
RAW TELEMETRY
{
"sensor": {
"temperature": 27.8,
"distance": 36
},
"phone": {
"activity": "STILL",
"battery": 82,
"location": [32.72, -117.16]
}
}
genieX
Qwen3-4B
PLAIN-LANGUAGE SUMMARY
“You're currently stationary, indoors, with room-temperature conditions and nothing within a few centimeters in front of the sensor. Your phone is at 82% battery.”
If a live reading is unreachable, a labeled sample fallback is used instead — the summary always notes when data may be stale.

## Slide 6
LLM + MCP
One Tool Claude Can Call
Both sensor streams feed a single MCP tool — Claude calls it whenever a question depends on the real world.
Phone
UNO Q
context_builder
genieX LLM
MCP tool
Claude
get_physical_context() — called before answering any question that depends on the user's real-world situation.